## Slide 1
Computational Catalysis and Emerging Materials Laboratory
Multiscale catalyst design integrating DFT, machine-learning potentials, and descriptors
Seokhyun Choung
June 4, 2026

## Slide 2
01
Motivation
1.1
Why Study Catalysis Computationally
Reaching what experiments cannot
✓ Reaction intermediates live for only ps–ns, so in-situ observation is hard — computation delivers atomic-scale snapshots
✓ Active-site candidates explode to 10⁴–10⁶ combinations — purely experimental screening is too costly and slow
✓ Trace activity and selectivity back to their electronic-structure origin, distilling them into design principles
→ Computation accelerates hypothesis generation and candidate selection, letting experiments focus on validation — a closed loop.
Key idea: computation does not replace experiment — it narrows the search space

## Slide 3
02
Methodology
2.1
A Multiscale Computational Stack
DFT
Adsorption energies, transition states, and the d-band center from first principles. The accuracy benchmark (ground truth), but it stalls at the few-hundred-atom scale.
ML Potentials
MLIPs (NequIP, MACE) trained on DFT give DFT accuracy at MD speed — extending to nanoparticles, dynamics, and ensemble sampling.
Microkinetics
Feed computed energies into rate equations to compare turnover frequency, the rate-determining step, and reaction orders directly with experiment.
A pipeline that bridges scales — from atoms to nanoparticles to reactor conditions

## Slide 4
03
Design Principle
3.1
Descriptors and Scaling Relations
Compressing complex activity into a few variables
Scaling relations
Adsorbate energies are linearly coupled, so a single descriptor (e.g. O binding energy) can predict activity.
Sabatier volcano
Bind too weakly and nothing activates; bind too strongly and the surface poisons — an optimum exists.
1–2
governing descriptors
<0.2 eV
target prediction error
Next-generation design targets sites that break scaling — multimetallics and interfaces

## Slide 5
04
Workflow
4.1
From ML Screening to Experiment
① Generate
Combine compositions, facets, and defects into tens of thousands of candidate structures; pre-filter stability with an MLIP.
② Predict
Regress activity and selectivity with descriptors and graph neural networks; quantify uncertainty to actively pick the next calculation (active learning).
③ Validate
Synthesize and test only the top candidates, return the data, and retrain — a closed loop that accelerates discovery.
Case: alloy oxygen-reduction catalysts compressed from 10,000 candidates to ~10 experiments

## Slide 6
Thank You
Computation × machine learning narrows the search space of catalyst design